## Slide 1: Life cycle assessment of food products and production systems
Neus Sanjuán

## Slide 2: Towards ecological food production
The food production system is a large user of energy and natural resources.
The concept of sustainability has only been applied to a limited extent to agricultural and industrial food production.
In the future the production of foods should be based on a global, ecological view.

## Slide 3: How can we evaluate the effects of food products on the environment?
Life Cycle Assessment

## Slide 4: What is Life Cycle Assessment?
LCA is a method for analysing and assessing the environmental loadings and effects caused by a product, process or service throughout its life cycle or lifetime

## Slide 5
Packaging
Transport
Processing
Retailer
Consumption
Agriculture
Waste
treatment
Waste

## Slide 6: Why to use Life Cycle Assessment?
because it is product oriented,
because it is integrative,
because it is scientific and quantitative

## Slide 7: Structure of LCA studies
Analysis:
  Goal definition and scoping
  Inventory analysis
Assessment:
  Impact assessment
    3a. Classification
    3b. Characterization
    3c. Valuation
  Interpretation and improvement analysis

## Slide 8
Life Cycle Assessment according to UNE-EN ISO 14040 (1997)
Goal and scope definition
Inventory analysis
Impact assessment
Interpretation
Direct applications:
Product improvement and development
Strategic planning
Public policy making
Marketing
Other

## Slide 9: Goal and scope definition
Goal: determining the use to which the environmental analysis will be put and assessing what can it and cannot be used.
Scope: to identify and to define the object of the assessment and to limit it to include which is significant for the goal of the LCA.
Definition of functional unit and system boundaries

## Slide 10: Inventory analysis
Implies gathering all the environmentally relevant information about the processes/activities included in the system limits.
The data gathered for each activity comprise: raw materials, products, energy use, emissions into the air and water and solid waste.
Data sources include:
  Internal company and public statistics
  Legislation, e.g. regarding permitted air emissions
  Waste management companies
  Reports of LCA carried out and similar projects
  Estimates, assumptions and theoretical values
  Open data bases for use in LCA

## Slide 11: Impact assessment
The effects originated by the resource consumption and the generated emissions are grouped and quantified in impact categories that can be weighted according to its importance.
The objective is to evaluate the importance of the potential environmental impacts using the results of the inventory analysis.
The interpretation must be based on the available background knowledge of the environment, resources and working environment, and it must show which of the exchanges are significant and how great their contributions can be.

## Slide 12
 | Impact categories | Suggested end points
Consumption of resources | Energy (renewable/nonrenewable) | MJ
 | Raw materials (renewable/nonrenewable) | % reserve, Sb equivalents
 | Land use | km2
Global effects | Global warming | g equivalents CO2
 | Ozone depletion | g eq. CFC-11
Regional effects | Acidification | g equivalents H+ g equivalents SO2
 | Eutrophication | g equivalents NO3-
 | Photo-oxidant formation | g equivalents C2H4
 | Toxicity (human) | g eq. 1,4-diclhorbenzene, DALY
 | Ecotoxicity | g eq. 1,4-diclhorbenzene, DALY

## Slide 13
THE INVENTORY TABLE
CLASIFICATION AND CHARACTERIZATION
EVALUATION
. . . .
. . . .
CO2
CH4
O3
CFC
NOx
…
SO2
NOx
NH4
…
NOx
NH4
P
COD
…
. . . . . . . . . . . . . . . . .
. . . . . . . . . . . . . . . . .
GLOBAL WARMING
ACIDIFICATION
NUTRIFICATION
ENVIRONMENTAL
INDEX

## Slide 14
Equivalence factors of some green-house gases
 |  | GWP (g CO2/g substance) |  |  | 
 |  | 20 years | 100 years | 200 years | 
Carbon dioxide | CO2 | 1 | 1 | 1 | 
Methane | CH4 | 62 | 25 | 8 | 
Nitric oxide | N2O | 290 | 320 | 180 | 
CFC 11 | CFCl3 | 5000 | 4000 | 1400 | 
CFC 12 | CF2Cl2 | 7900 | 8500 | 4200 | 
Carbon monoxide | CO | 4300 | 1700 | 520 | 

## Slide 15: Interpretation and Improvement analysis
The results are clearly presented; the necessity and the possibilities to reduce the environmental impact of the product are systematically evaluated.
The results from the inventory analysis are combined together with the impact assessment.

## Slide 16: Application of LCA to agricultural systems

## Slide 17: Special demands on LCA methodology when applied to food products
Goal definition and scoping:
  Choice of the system boundaries.
  Definition of the functional unit.
  Selection of allocation methods
Inventory analysis:
  Nutrient balances
  Pesticides fate analysis
  Capital goods
In impact assessment:
  The land use
  Animal welfare
  Water depletion
  Pesticides exposition and toxic effects

## Slide 18: Goal definition and scoping

## Slide 19: Systems and system boundaries
They must be specified in several dimensions:
  boundaries between the technological system and the nature
  geographical area
  time horizon considered
  production of capital goods

## Slide 20
Examples where system boundaries are crossed during bread production:
The soil and ground water receive emissions of pesticides and plant nutrients during the cultivation of wheat.
The ethanol released when baking is an emission into the air.
N
P
K
System boundary
System boundary
ethanol

## Slide 21: System boundaries
Soil within or outside the system? It is difficult to determine the system boundary between the technological system and the nature; agricultural production takes place in nature itself and is actually a part of the environmental system.
Soil is an integrant part of farming systems, and equivalent to other ancillaries in industrial systems. It differs from the common treatment of ancillaries because the soil is not consumed; but it may leave the system with properties that differ from those at the beginning of the time period under analysis.

## Slide 22: Functional unit
The functional unit is defined as quantified performance of a product system for use as a reference unit in an LCA study.
It is an amount of the final product system that performs a certain, measurable, function.
Is the unit to which all the environmental loadings are related.
In order to compare two products or systems they must fulfil the same functions.

## Slide 23: Functional unit
Relevant aspects to consider in the process of defining the functional unit:
  The function or the service of a food-producing system
  Additional functions of agricultural systems
  The spatial representativeness of the system.
  The temporal representativeness of the system.
  Performance of the system in relation to the specified functional unit.

## Slide 24
System: milk packaging
Functional unit: the quantity (kg) of packaging material used to deliver 1 L of beverage

## Slide 25
1005 kg ECM
organic milk
System: milk
Functional unit: 1000 kg energy corrected milk (ECM) leaving the farm gate. ECM is a correction factor used by the dairy industry: it considers both the fat and the protein content of milk
1000 kg ECM
conventional milk

## Slide 26
Functional unit | Unit | Farming intensity |  | 
 |  | Intensive | Extensive | Organic
Farm | t | 306 | 239 | 165
Area | t/ha | 9.4 | 7.0 | 6.3
Livestock | t/LU | 138 | 129 | 86.5
Product (milk) | t/t | 1.3 | 1.0 | 1.3
Emission of CO2-equivalents of different farming intensities depending on the functional unit chosen of the Allgäu LCA (Haas et al., 2000)

## Slide 27: Allocation procedures
The allocation procedures are methods used to distribute environmental loads among products.
They are necessary when a production process yields more than one product and quantitative models that link inputs to outputs are not available.
Allocation should be avoided whenever possible

## Slide 28
Production of fertilisers, diesel, pesticide, seeds
Cultivation of sugar beets
sugar industry
Cultivation of soybeans
oil extraction industry
oil
sugar
Co-products from sugar industry
Co-products from oil industry
The dairy farm
milk meat

## Slide 29
Crop | Products | Mass allocation % | Price allocation %
sugar beet | Sugar, beet pulp, molasses | 66 22 12 | 83 11 6
soybean | Oil, meal | 20 80 | 69 31
Mass and price ratio of ingredients in dairy concentrate feed (Cederberg and Mattson, 2000).

## Slide 30: Allocation: crop rotation and fertilization
How to consider interaction between crops in the rotation?
Ideally all the crops in a crop rotation system should be studied, since a crop may be influenced by the previous crops; the environmental loads should then be allocated among the different crops.

## Slide 31: Allocation: crop rotation and fertilization (van Zeits et al., 1999)
Farmers usually apply nitrogen fertilisers separately for each crop. Environmental impacts caused by application of N fertilisers can be fully allocated to the crop of application.
Phosphate and potassium do not easily leach to ground water: overfertilising one crop may be a benefit to following crops.

## Slide 32
production of manure
storage and transport to farm
application of animal manure
Nmin Norg P2O5 K2O organic matter
to crop production

## Slide 33: Allocation: crop rotation and fertilization (van Zeits et al., 1999)
Application of animal manure is multi-output process: Nmin, Norg, P2O5, K2O, organic matter.
Nmin and Norg first year available should be allocated to the crop of application. Norg following years available should be allocated to all crops in the rotation.
P2O5 and K2O the same allocation principles as for chemical fertilisers.
Organic matter benefits soil structure and soil life. All crops profit from this. So impacts should be allocated to all crops. The same for green manure.

## Slide 34: Life cycle inventory

## Slide 35: Inventory analysis
There are many factors that have a considerable bear and must be taken into account when carrying out the LCI.
Environmental interventions
Physical site
conditions
e.g.: soil’s buffer
capacity, permeability, weather, etc.
Producer’s technique
e.g.: time devoted to operations, election of active ingredients and fertilizer, etc.
Technology type
(e.g.: organic production, integrated, etc.)
Type of
inputs
Specific substance and amounts
Predicted
emissions
Site-dependency
System characteristics

## Slide 36: Pesticides fate analysis
Main difference between pesticides and other pollutants: pesticides are directly applied in the biosphere in order to control some life forma, while the seconds reach the environment indirectly.
Factors affecting pesticide fate:
  Application: dose and system
  Transport: substance type, climatology, plant morphology, area of aquatic and terrestrial surfaces
  Fate: physic-chemical characteristics of the pesticide and degradability, soil properties, and microorganism metabolism
  Exposition: the impact will be determined by the number of individuals exposed
  Effect: sensibility of the exposed population

## Slide 37: Impact assessment

## Slide 38: Land use
Until now the area occupied by a system (e.g. ha·year) has been considered as an indicator of “land use”.
Some studies show the importance of defining soil quality indicators taking into account:
  The decrease of soil quality (yield, organic matter content, salinization, erosion,...)
  Effects on biodiversity
There is no an internationally accepted indicator for this impact category.
This is one of the key aspects of the working group of the Life Cycle Iniciative (UNEP-SETAC) about Impact Assessments together with water consumption. More information in: http://unep.greenriver.org/init/LCA/resources.html

## Slide 39: Water use
Use of water may be considered as a resource depletion and/or disturbance impact
As a resource issue, relevant aspects for consideration are:
  Total use of water
  Use of surface water versus groundwater
  Temporary versus permanent removal of water from sources
  Use of water taken from the environment versus use of recycled water
  Total use of water in relation to water supplies in particular regions
As a disturbance impact, “harmful” use of water is assessed as use that causes desiccation.

## Slide 40: Pesticides exposition and toxic effects
Different methods have been proposed in LCA for the calculation of potential toxicity of substances.
Most of them does not take into account the toxicity caused by food ingestion and do not include many authorized pesticides.
The most known methods: Critical Surface Time (CST) (Jolliet, 1996), USES-LCA (Huigbregts et al., 2000), IMPACT 2002+ (Jolliet et al., 2002)
The webpage of the european project OMNIITOX (www.omniitox.net) presents the nowadays situation of toxicity analysis in LCA, including local factors.

## Slide 41: Livestock welfare
Although welfare of livestock should be an important issue in decision-making, it is debatable whether it should be included as an impact category in LCA.
The debate concerns whether animal welfare is regarded as environmental issue or not according to interpretation of that term in LCA.
Flagging up this aspect in a qualitative way during the Interpretation phase may be sufficient.